## Slide 1: S9 – AcS Detailed Design

## Slide 2: Agenda
Activation System Review
Activation System Architecture
Provisioning Subscriber Data
Activation Use Cases and Call Flows
Viewing Activated Subscribers
Client Configuration Data

## Slide 3: Activation System Review
What does the Activation System do?
  Checks that the user is who they say they are and that they are authorized for the service
  Provides configuration data and user credentials to the VoWiFi App
  Manages the user database
  Performs Reconfiguration of the App when configuration data is modified
The Activation procedure executes when the App is first run
  App contacts the Activation System, authenticates and requests configuration data
  If successful, the App receives configuration data and credentials
  Otherwise the activation procedure fails and the user must restart the activation process
The Reconfiguration procedure executes periodically
  App returns to the Activation Server every N days to check for new configuration data
  Similarly, App checks for new configuration data if unable to register with network

## Slide 4: Architecture

## Slide 5: Activation System Architecture
Highly scalable HA architecture:
Activation Server (AcS)
  The Activation Server presents an HTTP(s) interface towards the App to handle the App activation process
Home Subscriber Manager (HSM)
  Provides managed access to the Home Subscriber Database
  Presents an XML/HTTP interface towards the network to interface with the MNOs Service Provisioning platform
Home Subscriber Database (HSDB)
  High performance database for storage of user records and credentials
Admin Portal (AP)
  Provides Configuration, Fault & Performance management for the Activation System
Active System
XML/HTTP(s)
Interface to provisioning system
Activation
Server
(AcS)
Home Subscriber
Database
Home Subscriber
Database
Home Subscriber
Database
Home Subscriber Manager (HSM)
Admin
Portal
(AP)
Activation
Server
(AcS)
Home Subscriber Manager (HSM)
Admin
Portal
(AP)
Standby System
SYNC
HTTP(s)
interface to VoWiFi app
Fault & configuration management

## Slide 6: Cassandra Key Feature Set
Decentralized
  Every node in the cluster has same role. No single point of failure since data is distributed across the cluster (each node contains different data)
Replication support and Multi Data Center Replication
  Designed as a distributed architecture for deployment of large number of nodes across multiple data centers
  Flexibility in handling redundancy for failover and disaster recovery
Scalability
  Read and Write throughput increase linearly as new nodes are added
Fault-tolerant
  Data is automatically replicated to multiple nodes for fault tolerance. Failed nodes can be replaced with no down time
Query language
  CQL (Cassandra Query Language) – simple API for Cassandra access

## Slide 7: Server Platform Software
Application | AcS/HSM | Admin Portal | HSDB (Available in Release 10)
Taqua Platform Layer | T7100 |  | Apache Cassandra
Guest Operating System | RedHat Enterprise 6.7 |  | Redhat Enterprise 7.x
Hypervisor Option | VMWare vSphere Hypervisor (ESXi) 6.x |  | 
Subscriber Provisioning
Subscriber Provisioning
Subscriber Provisioning

## Slide 8: AcS Network Architecture
Seven (7) VMware-based Virtual Machines
Six (6) VLANs
Management
  HTTP/S, SSH, SNMP, NTP
Activation
  HTTP/S
IPC1/2
  High-Availability, Data Synchronization
RPC
  Subscriber Data Reads and Writes
Gossip
  Intra-cluster data exchange and synchronization

## Slide 9: Admin Portal VLANs and Protocols

## Slide 10: AcS VLANs and Protocols

## Slide 11: HSDB VLANs and Protocols

## Slide 12: Provisioning

## Slide 13: Provisioning Modes
Auto-Provisioned
  All subscribers within a PLMN are allowed to perform activation, i.e. subscribers whose PLMN identifier (MCC+MNC) matches the provisioned PLMN-Id list.
  The Activation Server generates subscriber data using the parameters provided by the client at the time of activation and the operator-configured template in the AcS.
Pre-Provisioned
  Only pre-provisioned subscribers are allowed to perform activation.
  The subscribers are pre-provisioned in the HSDB by the Service Provider’s Provisioning System.
  The Activation Server verifies the IMSI and MSISDN provided by the client with the pre-provisioned data.

## Slide 14: Auto-Provisioning
AcS will automatically create EAP and IMS credentials
  SIP Digest Username/Password
  EAP-MSCHAPv2 Username/Password
AcS will automatically create IMS Identities
  IMPU (IMS Public Identity)
  IMPI (IMS Private Identity)
Static passwords
All configuration data is sent to client (over secure channel) during Activation

## Slide 15: Activation

## Slide 16: Activation Methods - Comparison
AcS auto-generates subscriber data and stores in HSDB
PS network adds MSISDN to HTTP header
App contacts AcS over PS network
Activation over Cellular
(AoC)
AcS sends configuration data to VoWiFi App
AcS auto-generates subscriber data and stores in HSDB
AcS sends SMS with OTP to app host device, app sends OTP to AcS
App contacts AcS over Internet
Activation over Internet
(AoI)
AcS sends configuration data to VoWiFi App
Authentication
Network Access
Claro’s
Activation Method

## Slide 17: Activation Phases
Activation consists of two phases.
Phase 1
  Unencrypted HTTP request
  User authenticated by Cellular Data network which inserts the user’s MSISDN into the body of the request and forwards to AcS.
  AcS sends a response containing an http cookie to the Activation Client.
Phase 2
  Encrypted HTTPS request
  Cookie is verified
  AcS creates configuration data for new subscriber.
  AcS sends a response containing the configuration data.

## Slide 18: Client Reconfiguration
The Activation System is also responsible for reconfiguration of the Client
Configuration checking occurs when:
  The validity period of the current client configuration has expired (if set)
  The Client is unable to register with the network for N times (for certain error codes)

## Slide 19: Activation Call Flows

## Slide 20: Call Flow Use Cases
Initial Activation
Re-configuration
SIM / IMSI Change
MSISDN Change
User Deletion and Deactivation
Assumptions for call flows
Auto-Provisioning
Activation over Cellular (AoC)
Common SIP Digest password for all users
Common MSCHAPv2 password for all users
Both passwords will be statically configured in the Activation Server

## Slide 21: Initial Activation – Phase 1
2a. DNS Query (AS FQDN)
1. Check UE as cellular connection
Activation
Server
DNS
HSD
2b. DNS Response (AS IP/Port)
3. http GET Activation-URL (no parameters)
P-GW
4. HHE: Add MS-ISDN to HTTP Header
5. http GET Activation-URL (MS-ISDN header and no parameters)
7. Check local record for MS-ISDN does not exist
6a. Query Subscriber Record (key)
6b. Response
8. 200 OK (cookie A)
Sonus
Client
9. Store {MS-ISDN, Cookie A} & Start Timer

## Slide 22: Initial Activation – Phase 2
16b. Response
16a. Create Subscriber Record (key, data)
10. Establish TLS connection to Activation Server
11. https GET Activation-URL (ver=0, request parameters)
12. Stop Timer. Check Cookie A
Activation
Server
HSD
P-GW
Sonus
Client
17. 200 OK (token, Configuration Data)
19. Release TLS Connection
18. Store Data
15. Generate Token
13. Verify PLMN
14. Check Device Blacklist
20. Begin IMS Registration Procedures

## Slide 23: Reconfiguration
Activation
Server
HSD
P-GW
Sonus
Client
1. Check UE has cellular connection
2. http GET Activation-URL (no parameters)
3. HHE: Add MS-ISDN to HTTP Header
4. http GET Activation-URL (no parameters)
5. 200 OK (cookie A)
6. Store {MS-ISDN, Cookie A} & Start Timer
7. Establish TLS connection to Activation Server
8. https GET Activation-URL (version>0, request parameters)
9. Stop Timer. Check Cookie A
12. Check Config version
13. 200 OK (token, Configuration Data)
14. Store Data
15. Release TLS connection to Activation Server
11b. Response
11a. Query Sub Record (key, data)
Phase 1
Phase 2
ConfigValidity timer expires
10. Check Device Blacklist

## Slide 24: SIM / IMSI Change
1. Client Activated and NOT Registered
Activation
Server
HSD
5. http GET Activation-URL (no parameters)
P-GW
6. HHE: Add MS-ISDN to HTTP Header
(New MSISDN/IMSI pairing)
7. http GET Activation-URL (MS-ISDN header and no parameters)
Sonus
Client
2. New SIM Inserted
3. All previously stored configuration data is automatically deleted
4. Begin Initial Activation Procedures
11. Complete Phase 2 Initial Activation procedures
9. Remove existing MSISDN and IMSI records
8a. Query Subscriber Record (key)
8b. Response
9a. Delete Subscriber Record (key)
9b. Response
10. 200 OK (cookie A)

## Slide 25: MSISDN Change – Part 1: Update active SIP registration
Activation
Server
Nokia PGW/UDC/HSS
P/I/S-CSCF
HSD
2. Change MSISDN
3. Registration-Termination-Request
4. Registration-Termination-Answer
5. SIP NOTIFY (Event:reg, <contact state=”terminated”, event=”rejected”)
6. 200 OK
1. Client Activated and Registered
Sonus
Client
7. Client IPSec Tunnel is terminated
8. Client re-establishes IPSec
9. Client registers with IMS and receives new MSISDN in 200OK (P-Associated-URI)

## Slide 26: MSISDN Change – Part 2: Update AcS Subscriber Data
Activation
Server
HSD
P-GW
Sonus
Client
1. Check UE has cellular connection
2. http GET Activation-URL (no parameters)
3. HHE: Add MS-ISDN to HTTP Header
(New MSISDN/IMSI pairing)
4. http GET Activation-URL (MS-ISDN header and no parameters)
7. 200 OK (cookie A)
8. Store {MS-ISDN, Cookie A} & Start Timer
5a. Query Subscriber Record (key)
5b. Response
6a. Delete Subscriber Record (key)
6b. Response
9. Complete Phase 2 Initial Activation procedures
ConfigValidity timer expires
6. Remove existing MSISDN and IMSI records

## Slide 27: Subscriber Deletion and Deactivation
Activation
Server
Nokia PGW/UDC/HSS
P/I/S-CSCF
HSD
2. Delete User
3. Registration-Termination-Request
4. Registration-Termination-Answer
5. SIP NOTIFY (Event:reg, <contact state=”terminated”, event=”rejected”)
6. 200 OK
1. Client Activated and Registered
9. Reconfiguration procedure: HTTP GET (version=0)
11. Client De-activated; Goes back to the initial activation screen
Sonus
Client
P-GW
10. No response due to PDN authentication failure
7. Client IPSec Tunnel is terminated
8. Client attempts IPSec establishment ‘n’ times; Failure

## Slide 28: Viewing Activated Subscribers

## Slide 29: List of Activated Subscribers

## Slide 30: Activated Subscriber Record

## Slide 31: Client Configuration Data

## Slide 32: Client Configuration Data
Element | Content
Version | Configuration version (integer value, 0 or a positive integer)
Validity (version) | Pre-configured. Validity of current configuration (in seconds, 0 or a positive integer)
Token | Generated by the Activation Server. Token to be used in subsequent re-configuration requests, String (12 min, 24 max)
Validity (token) | Pre-configured. Validity of token (in seconds, a positive integer). Default value = 31536000 seconds.
Private User Identity | Generated by the Activation Server from the IMSI. It has the format IMSI@home network domain. String (64 max)
Public User Identity | Generated by the Activation Server from MSISDN. It has the format sip:MSISDN@home network domain. String (64 max)
Home Network Domain Name | Pre-configured. A fully qualified domain name or IPv4 address. String (64 max).

## Slide 33: Client Configuration Data
Element | Content
PCSCFPort | Pre-configured. P-CSCF Port. Range 0 to 65535 with a default value of 5060.
wifiSignalling | Pre-configured. SIP signalling transport protocol over WiFi: SIPoTCP, SIPoTLS, SIPoUDP, SIPoUDPoIPSec, SIPoTCPoIPSec
wifiRTMedia | Pre-configured. Transport protocol used to carry real time media over WiFi: RTP or SRTP.
TLSPort | Pre-configured. TLS port number for SIP signalling Range 0 to 65535 with a default value of 5061
VoiceCallAuth | Pre-configured. Enables/Disables MMTEL telephony (wifi-calling) service. An unsigned 32 bit integer value that is mapped to a bit array indicating the radio technologies in which the service can be initiated.
NetworkName | Pre-configured. Name of the operator network that provides the service. String (32 max)

## Slide 34: Client Configuration Data
Element | Content
SMS_Over_IP_Networks_Indication | Pre-configured. Indicates preference for selection of the domain to be used for short message service (SMS) originated by the UE 0 – Indicates that the SMS service is not to be invoked over IP networks. 1 – Indicates that the SMS service is preferred to be invoked over IP networks.
SMS_SegmentSize | Pre-configured. Maximum size of a short message segment in octets. Range is 70 to 140 octets and the default value is 140.
SM-SC_Uri | Pre-configured. SIP URI of short message service centre (SM-SC) to submit mobile originating short message over IP. String (64 max).
Timer_TR1M | Pre-configured. Timer value in seconds to wait for response after submitting mobile originating short message over IP. Range is 35 to 45 seconds with a default value of 40 seconds.
Timer_CW | Pre-configured. Timer value in seconds to limit the duration of a call in communications-waiting condition. Range is 10 to 60 seconds with a default value of 30 seconds.

## Slide 35: Client Configuration Data
Element | Content
SecondaryIMSI | Pre-configured. A secondary IMSI of the subscriber in addition to the primary IMSI. The client will be operational (provide service) only if the IMSI read from SIM matches either the primary or secondary IMSI values. The secondary IMSI value for a subscriber is obtained from the HSM. String (15 max). A null string is returned if secondary IMSI is not present in HSM.
DefaultCellIdentity | Pre-configured. Default cell identity to be used in P-Access-Network-Info header. Encoded as a text string as follows: MNC(3 digits) + MCC(2 or 3 digits) + LAC (2 octets) + UMTS cell identity (5 octets) MNC(3 digits) + MCC (2 or 3 digits) +, LAC(2 octets) + cell identity(2 octets)
AccessType | Pre-configured. Access type to be used in P-Access-Network-Info header. Possible values are “3GPP-GERAN”, “3GPP-UTRAN-FDD”, “3GPP2-1X”..
PullbackAuth | Pre-configured. Enables/Disables pullback procedure. 0: Disabled 1: Enabled

## Slide 36: Client Configuration Data
Element | Content
NumberExpansionAuth | Pre-configured. Enables/Disables phone number expansion to E.164 format. 0: Disabled 1: Enabled
MinDigits | Pre-configured. Minimum number of digits in the phone number to perform number expansion. Valid only if number expansion is enabled.
roveInTimer | Pre-configured. When the UE roves out, it starts roveInTimer and will not rove-in until this timer has expired, unless the UE has detected loss of cellular coverage. Range is 5 to 60 seconds and the default value is 15 seconds.
roveInWiFiRSSI | Pre-configured. UE will rove-in to WiFi network when WiFi signal strength is above this value. Range is 0 to -200 and the default is -75.
roveOutWiFiRSSI | Pre-configured. UE will rove-out from WiFi network when WiFi signal strength is below this value. Range is 0 to -200 and the default is -85.

## Slide 37: Client Configuration Data
Element | Content
roveInCellularRSSI | Pre-configured. UE will rove-in to WiFi network when cellular signal strength is below this value. The value range of roveOutCellularRSSI is 0 to -200 and the default value is 0.
roveOutSmsAddress | Pre-configured. UE, on rove-out, sends an SMS to roveOutSmsAddress to cause a location update procedure on cellular network. The default value of the roveOutSmsAddress is a null string.
Conference_Factory_URI | Pre-configured. SIP URI used for setting up an IMS conference.
MaxUsers | Pre-configured. Maximum number of users allowed to participate in an IMS conference. Range is 2 to 6 with a default value of 3.
LocationInfoAuth | Pre-configured. Authorization to include location configuration information element in the P-Access-Network-Info header if Cell-Id is not available. 0: Disabled 1: Enabled

## Slide 38: Client Configuration Data
Element | Content
Expiry | Pre-configured. The date and time in UTC timezone when the current client version expires (encoded in ISO 8601 format, YYYY-MM-DDTHH:MM:SSZ). The Activation server uses the following rule to decide on the expiry value. 1. The Activation Server has a provisioned list of (client_version, expiry) pairs sorted by ascending client_version values. 2. Find all the pairs whose client_version is greater than or equal to the client_version received in the first activation request and use expiry value of the pair with the lowest client_version. 3. If no pair is found, use an expiry value of 2100-01-01T00:00:00Z.
MMSC_URL | Pre-configured. URL of Multimedia Messaging Service Centre. String (64 max)
MMS_Proxy | Pre-configured. Domain name or IP address of MMS proxy. String (64 max)
MMS_Port | Pre-configured. Port number of MMSC or MMS proxy server. Range is 0 to 65535.
MMS_Maxsize | Pre-configured. The maximum size of Multimedia Message in Kilobyte (KB) that can be sent. Range is 0 to 10000.

## Slide 39: Client Configuration Data
Element | Content
HandoutToCS | Pre-configured. The type of WiFi to cellular handout supported by UE. The values are disabled, manual, automatic.
HandoutToCSWiFiRSSI | Pre-configured. UE will handout to cellular network when the WiFi signal strength is below this value. The range is -200 to 0 with a default value of -200. A minimum value of -200 effectively disables handout based on WiFi RSSI.
HandoutToCSDlPktLoss | Pre-configured. UE will handout to cellular network when the downlink packet loss (in percentage) is above this value. The range is 0 to 100 with a default value of 5. A maximum value of 100 disables handout based on packet loss
HandoutToCSDlJitter | Pre-configured. UE will handout to cellular network when the downlink jitter (in ms) is above this value. The range is 0 to 1000 with a default value of 5. A maximum value of 1000 effectively disables handout based on DL jitter.
SBCCert_URL | Pre-configured. URL for root or intermediate certificate of a Certificate Authority (CA) to authenticate a session border controller (SBC). String (64 max). A value of NULL indicates that no certificate is available.
SeGWCert_URL | Pre-configured. URL for root or intermediate certificate of a Certificate Authority (CA) to authenticate a security gateway (SeGW). String (64 max). A value of NULL indicates that no certificate is available.

## Slide 40: Client Configuration Data
Element | Content
MMICommandRouting | Pre-configured. UE behaviour when it detects MMI command in dialled string. Possible values are “routeOverCellular”, “routeOverIP” and “disabled” with a default value of “disabled”.
MmiCommandRoveOutTime | Pre-configured. The amount of time UE remains roved out after it detects an MMI command. The range is 30 to 180 seconds with a default value of 60 seconds.
SeGW_Address | Pre-configured. A fully qualified domain name or IPv4 address of security gateway. String (64 max)
EAPMethod | Pre-configured. The Extensible Authentication Protocol (EAP) authentication method. Possible values are “EAP-MD5”, “EAP-MSCHAPv2”, EAP-TLS”.
EAPPwd | Pre-configured. The password to be used in EAP procedures. String (64 max)
IKEEncryptionAlgorithm | Pre-configured. The encryption algorithm to be used for Internet Key Exchange (IKE) protocol. Possible values are “3DES-CBC”, “AES-CBC-128”.
IKEIntegrityAlgorithm | Pre-configured. The integrity algorithm to be used for Internet Key Exchange (IKE) protocol. Possible values are “HMAC-SHA1-96”, “AES-XCBC-MAC-96”.
IKEPseudorandomFunction | Pre-configured. The pseudorandom function to be used for Internet Key Exchange (IKE) protocol. Possible values are “HMAC-SHA1”, “AES-XCBC-PRF-128”.

## Slide 41: Client Configuration Data
Element | Content
IKEDiffieHellmanGroup | Pre-configured. The Diffie-Hellman group to be used for Internet Key Exchange (IKE) protocol. Possible values are “2”, “14”.
IKEKeyLifetime | Pre-configured. The lifetime for IKE Security Association keys. A rekeying procedure is performed on its expiry. The range is 300 seconds to 86400 seconds with a default value of 28800 seconds. A value of 0 indicates that rekeying is disabled.
ESPEncryptionAlgorithm | Pre-configured. The encryption algorithm to be used for IP Encapsulating Security Payload (ESP) protocol. Possible values are “3DES-CBC”, “AES-CBC-128”, “AES-CTR”.
ESPIntegrityAlgorithm | Pre-configured. The integrity algorithm to be used for IP Encapsulating Security Payload (ESP) protocol. Possible values are “HMAC-SHA1-96”, “AES-XCBC-MAC-96”, “HMAC-MD5-96”.
ESPKeyLifetime | Pre-configured. The lifetime for ESP Security Association keys. A rekeying procedure is performed on its expiry. The range is 300 seconds to 86400 seconds with a default value of 28800 seconds. A value of 0 indicates that rekeying is disabled.
DPDIdleTimer | Pre-configured. When UE does not receive an inbound ESP packet for idle timer period it shall start a DPD procedure. The range is 20 seconds to 300 seconds with a default value of 60seconds. A value of 0 indicates that DPD is disabled.

## Slide 42: Client Configuration Data
Element | Content
DSCPMarking | Pre-configured. Enable/Disable DSCP marking of signalling and media packets. 0: Disabled 1: Enabled (default value) The Activation Server obtains the DSCPMarking value by looking up a device configuration table using the “terminal_vendor”, “terminal_model” and “terminal_sw_version” parameters in the activation request. If not found in the table, the default value is returned.
SIPSignallingDSCP | Pre-configured. DSCP value used for SIP signalling packets. The range is from 0 to 56 with a default value of 32.
RTMediaDSCP | Pre-configured. DSCP value used for real-time media packets. The range is from 0 to 56 with a default value of 46.
AudioMode | Pre-configured. Audio mode type. Possible values are “IN-CALL” , “IN-COMMUNICATION” (default value). The Activation Server obtains the audiomode value by looking up a device configuration table using “terminal_vendor”, “terminal_model” and “terminal_sw_version” parameters in the activation request. If not found in the table the default value is returned”

## Slide 43: Client Configuration Data
Element | Content
HandsetUplinkAudioGain | Pre-configured. Audio gain value. The range is from 1 to 6 with a default value of 2. The Activation Server obtains the audiogain value by looking up a device configuration table using the “terminal_vendor”, “terminal_model” and “terminal_sw_version” parameters in the activation request. If not found in the table the default value is returned.

## Slide 44: Thank You
Sonus Networks
978-614-8100 Office
978-614-8100 Mobile
email@sonusnet.com
www.sonus.net